## Slide 1: ALTERA
MICROPROCESSOR GROUP PRESENTATION

## Slide 2: DESIGN OF A 16-BIT CISC CPU

## Slide 3: ARCHITECTURE
CISC – Complex Instruction Set Computer
Von Neumann Architecture

## Slide 4: IMPLEMENTATION OF DESIGN
ALU
Control Unit
General Purpose Registers
CPU

## Slide 5: INSTRUCTION FORMAT
For R-type : Arithmetic, Logic
R-operation - 3 registers no immediate
For I- type : Load/Store, immediate
I - operation - 1 register and immediate
NB: Store 2 : 2 registers and RT contains the address
For J-type (targeted address) : jump
J - operation - 0 registers and address

## Slide 6: INSTRUCTION FORMAT
Opcode | Source 1 | Source 2 | Destination
0000 | 0000 | 0000 | 0000
ALU
Opcode | Target | Source | Don’t care
0000 | 0000 | 0000 | XXXX
MOVR
Opcode | Target | Immediate
0000 | 0000 | 0000 00000
MOVI
Opcode | Target | Address
0000 | 0000 | 0000 00000
Opcode | Target | Address
0000 | 0000 | 0000 00000
LOAD
STORE1

## Slide 7
Opcode | Source1 | Source2(always 0000) | Address(Destination)
0000 | 0000 | 0000 | 0000
STORE2
Opcode | Don’t care | Address
0000 | XXXX | 0000 00000
JMP
Opcode | Don’t care | Address
0000 | XXXX | 0000 00000
JMPZ
Opcode | Don’t care | Address
0000 | XXXX | 0000 00000
JMPN

## Slide 8: Instructions
Instruction Set Architecture
ADD
SUB
MULT
DIV
SHL
SHR
AND
OR
Extended Instruction Set Architecture
ADDC
EXCHANGE
MOVR
MOVI
LOAD
STORE
JMP
JMPZ
JMPN
NOP/HALT

## Slide 9
OPCODE | INSTRUCTION | MEANING
0000 | ADD | Addition Operation
0001 | SUB | Subtraction Operation
0010 | MULT | Multiplication Operation
0011 | DIV | Division Operation
0100 | SHL | Shift Left
0101 | SHR | Shift Right
0110 | AND | AND Operation
0111 | OR | OR Operation
INSTRUCTION SET

## Slide 10
OPCODE | INSTRUCTION | MEANING
1000 | MOVR | Move ( Register )
1001 | MOVI | Move ( Immediate )
1010 | LOAD | Read from Memory
1011 | STORE | Write to Memory
1100 | JMP | Unconditional Jump
1101 | JMPZ | Jump if zero
1110 | JMPN | Jump if negative
1111 | HALT/NOP | Stop the CPU / No operation
INSTRUCTION SET

## Slide 11: Hardware Realization
The main components that make used in our processor.

## Slide 12: Components of the CPU
1
2
3
4
5
Read from or write to on a short term basis
RAM
Generate control signals to control the flow of information within the CPU
Control Unit
Holds the instructions address
Program Counter
High speed locations for storing information
Registers
Performs arithmetic operations
ALU

## Slide 13: THE ASSEMBLER
The Assembler converts our assembly to machine code for the processor

## Slide 14
THE ASSEMBLER

## Slide 15
FIBONNACCI PROGRAM

## Slide 16
ARITHMETIC AND LOGIC UNIT

## Slide 17
CONTROL UNIT

## Slide 18
GENERAL PURPOSE REGISTERS

## Slide 19
CENTRAL PROCESSING UNIT